## Slide 1: IP Networking Basics
Open Sourcery

## Slide 2: What’s an internet?
An internet:
The Internet™:
“Can talk with one another…”
Notes: An internet is a collection of computers that can talk to one another. This is called a network, mainly to avoid confusion with the big internet. The Internet with a capital I is the worldwide network that we use every day.
But I mentioned that the computers can talk with one another…

## Slide 3: How can machines talk with one another?
Using agreed upon rules
A rule set called network protocol
Notes: How do they do that?
They do that using agreed upon rules. An analogy to these rules would be how, if you wanted to send a letter but left the address blank and without a stamp, the letter wouldn’t be sent.
We call a rule set that a network uses it’s network protocol.

## Slide 4: What is IP?
Internet Protocol (IPv4 and IPv6) — most widely used network protocol
Governs:
  Addressing
  Routing
  Structure of information
Notes: Now IP is just the “Internet Protocol” — the most widely used network protocol. You can find others being used in smaller use cases, and typically in legacy system.
This protocol governs addressing (how computers identify themselves to the world), routing (how information gets passed along until it hits the proper address), and structure of information.

## Slide 5: Packets
Information that is structured according to network rules
Just 1’s and 0’s, living their best life
Notes: Now, all packets are is information that’s structured according to network rules. It’s 1’s and 0’s living their best life.

## Slide 6: IP Header
20 bytes at the beginning of the message
Meta information
Header
Options
Data
Packet
Notes: Now, IP protocol requires every packet sent to contain the IP header: 20bytes of information at the beginning of the message. It contains meta information necessary for the packet to get where it needs to go.

## Slide 7: Big Idea: Encapsulation
Data doesn’t affect routing of info!
Can send anything over an IP network
Header
Options
Data
Packet
Doesn’t matter!
Notes: The big idea behind this structure is encapsulation: what the data is doesn’t matter to getting the data where it needs to go.

## Slide 8: DEMO TIME
Let’s trace a packet along the network!
If on windows, on your favorite terminal, run:
tracert google.com
If on mac or linux, on your favorite terminal, run:
traceroute google.com
Notes: So, let’s see a packet traveling along the network! Take out your laptops and let’s see this happen.
  If you’re on a windows machine, and if you can log onto grace, log onto grace now. This lets you run linux commands, which are a bit easier. If you don’t know what this means, don’t worry about it.
Run this command:
  Traceroute google.com —> linux or ma
  Tracert google.com —> windows. A lot slower for some reason
And tada, here your see your packet traversing the Internet, big I, in order to get to google.
So what traceroute does is a little complicated, but the big idea is that it sends a packet meant to diagnose things in the network and asks all machines that see it to respond.
Several things to note here:
  Information gets across the internet in a similar way to how a package gets shipped on Amazon: with many stops along the way in places like Iowa.
  Hops are what we call individual steps in going over the network, say from a warehouse in Iowa to a warehouse in Maryland. A packet is typically constrained to 30 hops, which is meant to ensure no packet circles the internet forever and gets dropped instead.
    And fun fact: this counter is in an IP header!
Now if we do another website, say bing, you might get these stars. What this means is that it hit a routine machine that isn’t configured to respond to the packet that we’re sending out. Traceroute sends out an ICMP packet, which is meant for diagnostics.
https://www.redhat.com/sysadmin/traceroute-finding-meaning#:~:text=If%20the%20traceroute%20command%20completes,an%20issue%20on%20the%20network. If I need to remember shit about traceroute
https://www.cs.ait.ac.th/~on/O/oreilly/tcpip/firewall/ch06_03.htm about packets and stuff

## Slide 9: Packet Types
Data can have structure too!
Often has its own meta info
IP Header has info about what type of packet is being sent
Header
Options
Data
Packet
Header
Data
Notes: Now, one thing that demo hinted as is that there are different types of packets — we sent one used for diagnostics.
Packets are differentiated by the structure of their data. There are different types of packets — TCP and UDP are very common ones
What type of packet is being sent is included in the big IP header
To reiterate though, all these packet types are conventions and rules that humans made so machines can actually talk to one another

## Slide 10: Ports
Notes: This section is easily the worst

## Slide 11: Motivation
Notes: So machines are receiving these packets constantly. They’re also constantly sending packets out
But how does a machine keep track of where packets should go? How does it ensure that when your discord app sends a request, that the data you get back goes pack to the discord app?

## Slide 12: Ports
“Virtual places” in OS where packets are sent from and to
Each port is connected to an application
80
64
53490
2165
20
200
333
Notes: So now, we gotta talk about ports.
Ports are, in a way, virtual places in the operating system where packets are sent from and to
In reality, it’s a way that the operating system sorts different types of packets
For example, different apps will “open up” ports in order to be able to send and receive messages

## Slide 13: Note: ports are NOT part of the IP header
Certain types of packets require ports
Because ports organize data within a machine: don’t matter outside of a machine.

## Slide 14: Types of Ports
Permanent — connected to permanent applications
  Often used to send data upon request
  Permanent ports have numbers with agreed upon meanings
  E.g. port 80, by convention, has HTML data
Ephemeral — for temporary requests
  Often used for requesting and receiving data from a permanent port
  Have high numbers, and are random

## Slide 15: DEMO TIME
Sending packets using Python!
Goal: ~experience~ ephemeral ports
Notes: First note: I’m currently using two VMS that I got as a part of one of my classes, so sadly this isn’t directly recreatable.
On one side, we have a container that’s going to receive UDP packets, a pretty simple type of packet that requires a port
  So here’s the code for receiving code. We have the IP address of where this is running

## Slide 16: Receiving
Opens port 5005 on local machine
Notes: First note: I’m currently using two VMS that I got as a part of one of my classes, so sadly this isn’t directly recreatable.
On one side, we have a container that’s going to receive UDP packets, a pretty simple type of packet that requires a port
  So here’s the code for receiving code. We have the IP address of where this is running

## Slide 17: Receiving
When it receives data, prints the IP + port it got it from, and the data
Notes: First note: I’m currently using two VMS that I got as a part of one of my classes, so sadly this isn’t directly recreatable.
On one side, we have a container that’s going to receive UDP packets, a pretty simple type of packet that requires a port
  So here’s the code for receiving code. We have the IP address of where this is running

## Slide 18: Sending
Targets opened port
Notes: First note: I’m currently using two VMS that I got as a part of one of my classes, so sadly this isn’t directly recreatable.
On one side, we have a container that’s going to receive UDP packets, a pretty simple type of packet that requires a port
  So here’s the code for receiving code. We have the IP address of where this is running

## Slide 19: Sending
Custom messages
Notes: First note: I’m currently using two VMS that I got as a part of one of my classes, so sadly this isn’t directly recreatable.
On one side, we have a container that’s going to receive UDP packets, a pretty simple type of packet that requires a port
  So here’s the code for receiving code. We have the IP address of where this is running

## Slide 20: Sending
Sends the message to the IP and port
Notes: First note: I’m currently using two VMS that I got as a part of one of my classes, so sadly this isn’t directly recreatable.
On one side, we have a container that’s going to receive UDP packets, a pretty simple type of packet that requires a port
  So here’s the code for receiving code. We have the IP address of where this is running

## Slide 21: Let’s see what port they come from!
Notes: First note: I’m currently using two VMS that I got as a part of one of my classes, so sadly this isn’t directly recreatable.
On one side, we have a container that’s going to receive UDP packets, a pretty simple type of packet that requires a port
  So here’s the code for receiving code. We have the IP address of where this is running

## Slide 22: IP Exhaustion and NAT

## Slide 23: IP(v4) Addresses
142.250.188.206
4 bytes — 32 bits

## Slide 24: How many IP Addresses are there?
232 = ~4.2 billion
But… um…

## Slide 25: IPv6 Addresses
4514:5776:90e3:d6bb:8565:bf9e:3f0e:2970
16 bytes — 128 bits
340 trillion trillion addresses!

## Slide 26: Are we using IPv6?
We’re transitioning
But we’re able to connect all those devices under IPv4
How?

## Slide 27: Your Router!

## Slide 28: What your router does
Self contained
Notes: Routers make all traffic go through one gateway to the big internet, and vice versa
Routers create networks that are completely separate from the big internet
They make all traffic from your machine to the Internet go through translation at the router
So, none of the machines in your little network have a public IP address

## Slide 29: Public and Private Addresses
192.168.1.5
192.168.1.9
192.168.1.42
192.168.1.1
128.8.27.57
Public Address
- Visible on Internet™
Private Addresses
- Only visible inside
Notes: The router has a public IP address that the Internet, big I, can see
Then, the router initializes a small, self contained network with private IP addresses
  Some Ips are reserved for private addresses. 192.168.x, 172.x, and 10.x are the most common ones
  This is why your IP almost always something like that

## Slide 30: Sending a packet
To: google
From: Lana

## Slide 31: Sending a packet
To: google
From: Lana

## Slide 32: Sending a packet
To: google
From: Lana

## Slide 33: Sending a packet
To: google
From: Router

## Slide 34: Sending a packet
To: google
From: Router
Google does NOT know that I sent this

## Slide 35: Sending a packet
To: Router
From: google

## Slide 36: Sending a packet
To: Router
From: google

## Slide 37: Sending a packet
To: Lana
From: google

## Slide 38: Sending a packet
To: Lana
From: google

## Slide 39: Public and Private Addresses
192.168.1.5
128.8.27.57
Notes: In reality, the “from” is your computer’s private IP address, while what the router replaces it with is the public IP address
So the addresses are, in a way, translated from private to public

## Slide 40: NAT — Network Address Translation
Notes: This is called Network Address Translation, because the IP addresses

## Slide 41: (QUICK) DEMO TIME
Seeing NAT happen
Notes: Use hostname -I to see the IP of the aces vm
And show that’s the receiving thought it received the message from a different IP
This is because a router is in the middle translating things

## Slide 42: Some Mechanics of NAT
Router has NAT table
Has different rules for translating different types of packets
Most often, creates an ephemeral port on the router to receive the responses

## Slide 43: Fun facts
NAT doesn’t increase security — a common myth
  But does make it easier to set up security, since all traffic goes through one bottleneck
  So, in general, private networks more secure
Can have many layers of NAT
Router stores NAT table in RAM, and routers have ~128 MB of RAM
  If RAM overflows, you have to restart your router!

## Slide 44: Application: Virtual Private Network
Depending on time, we’ll skip this~

## Slide 45: You’re a company, and you have sensitive info
Only a private network
Random cloud, like Google Drive
How do you get security of private network while allowing remoteness?

## Slide 46: Virtual Private Network
Tunnel, publicly
Computer now looks like it’s on the private network

## Slide 47: I wonder where you’ve seen this before…
I wonder…

## Slide 48: Commercial VPNs
Allow you to tunnel to a remote router and make it look like you’re based there
The principle behind VPNs allowing you to access geographically locked data!

## Slide 49: Cool: DNS
Depending on time, we’ll skip this~

## Slide 50: Domain Names
Domain name like “google.com” is an alias for google’s IP
How do we go from typing in “google.com” to getting it’s IP address?

## Slide 51: DNS — Domain Name System
DNS recursive resolver
- Assigned to you by router
Google.com?

## Slide 52: DNS — Domain Name System
First, looks in cache
If not in cache…
Google.com?

## Slide 53: DNS — Domain Name System
Asks the DNS root servers
Google.com?

## Slide 54: DNS — Domain Name System
Google.com?

## Slide 55: DNS — Domain Name System
142.250.188.206!

## Slide 56: DEMO
DIG
Aka
  Mac, linux: dig google.com
  Windows: nslookup google.com

## Slide 57: DNS — Domain Name System

## Slide 58: Yeah!! Go UMD!!
Lots of research is done using traffic we get from DNS
Dr. Dave Levin is one of the professors who’s invested in it

## Slide 59: A lot more to learn!
DNS specifics
Different types of packet/connection protocols
  TCP and the TCP handshake
  UDP
Network encryption — TLS handshake
How tunneling works
Firewalls in general
And more…

## Slide 60: Thank you!